What is Cathodic Protection and

Why Do You Need It?

Written by Captain Stanley G. Konz, A.M.S.

Electrochemical corrosion of metals is one of the most destructive processes

that affects a boat during its lifetime. Cathodic protection is designed to

prevent corrosion by altering a metal's electrochemical characteristics through

the application of electrical current by the use of ZINC ANODES or impressed

current.

Your boat's underwater metal fittings such as propellers, shafts, struts, and

thru-hulls are susceptible to electro- chemical corrosion.

There are several types of corrosive influences:

Galvanic Corrosion

Galvanic Corrosion occurs when two or more metals with different galvanic

voltages are electrically connected through a bonding system and by current

carrying fluid. It is the result of the more active metal's natural tendency to

give up electrical current to the less active metal. Galvanic corrosion may

occur in fresh or salt water, will not occur in pure water.

Stray Current Corrosion

Stray Current Corrosion occurs when underwater metals are energized by an

electrical current that has strayed from an electrical conductor or device powered

by a battery, generator or dock power. It is the result of an electrical fault.

Caustic Attack to Wood

Caustic Attack to Wood damage occurs from excessive cathodic protection. It

is the result of a lack of proper control of cathodic protection anodes, dissimilar

metals or an electrical fault.

Caustic Attack to Aluminum

Caustic Attack to Aluminum to an aluminum hull, stern drive or other aluminum

parts occurs from excessive cathodic protection. It is the result of a lack of

proper control of cathodic protection, dissimilar metals or an electrical fault.

If you have any questions, please feel free to contact us.

Captain Stanley G. Konz, A.M.S.

Maritime Vessel Surveying, Inc.

1-800-576-9116

captstan@boatquotes.com