| DIAGNOSTIC TOOLS Utilized by Maritime Vessel Surveying, Inc. We provide these services when they are needed and welcome our clients' presence while conducting the survey. INSPECTION USING MODERN DIAGNOSTIC EQUIPMENT |
| --- |
| CARBON MONOXIDE DETECTOR During sea trial tests for exhaust back drafting and penitrations of cabin spaces. DIGITAL TACKOMETER Electronic readings of RPM on engines and mechanical equipment. ELECTRONIC STETHOSCOPE Sound analyzing of engines and mechanical equipment ENGINE COMPRESSION GAUGE Testing on gas Engine/Generator INTERNAL (BORESCOPE) INSPECTIONS Allows inspection of inaccessible areas, behind ceilings, engine cylinders,marine gear and other equipment. MARINE MOISTURE METER Moisture Testing involving non-destructive moisture readings. Osmosis is a chemical breakdown in a laminate due to moisture ingress which ultimately results in delamination and blistering of the gelcoat Combined with sounding provides Osmosis Analysis.Indicates saturation of wooden structural systems, rot and determines the condition of wood boat planking and structural components. MILLIAMP MULTI METER Underwater mechanical and Hull Corrosion.Silver/Silver Chloride Half Cell Testing is an in-water corrosion test that determines susceptibility to galvanic and stray current corrosion, it is also an indication of the condition and proper operation of Zincs. | VIBRATION METER Testing and Analysis using vibration monitor to analyize motor mounts and shaft alignment. NON-CONTACT INFARED THERMOMETER Heat sensing to analyze exhaust systems, 12 and 120 volt electric systems. PRESSURE GAUGES Pressure testing of fuel tanks, water tanks and waste tanks. SPECTROMETRIC ENGINE FLUID ANALYSIS Sampling of and laboratory analysis of engine and mechanical equipment to indicate in parts per million of worn metal particles. TACHOMETER Digital readout of engine revolutions (RPM) under load to insure full power is produced according to manufacturers specifications. ULTRASONIC THICKNESS GAGE Ultrasonic testing, Non-destructive thickness measurement of steel, aluminum and fiberglass hulls Gauging steel and aluminum hulls. VIBRATION SENSOR (piezoelectric accelerometer) Please contact Maritime Vessel Surveying, Inc. at 1-800-576-9116 (toll free) or Email: CaptStan@boatquotes.com if you have any questions regarding these diagnostic tools. |